## Slide 1: Python, Motion Sensors and Data Fusion PyCon UK, 15 September 2016
Stephen Simmons
mail@stevesimmons.com
https://github.com/stevesimmons/pyconuk-motion-sensor-data-fusion

## Slide 2: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap

## Slide 3: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python

## Slide 4: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python
Motion sensors then and now – 1852, 1965, 2016
Example #1 – Wireless motion logging with BBC micro:bit

## Slide 5: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python
Motion sensors then and now – 1852, 1965, 2016
Example #1 – Wireless motion logging with BBC micro:bit
Data fusion – combining data from multiple sensors
Example #2 – micro:bit tilt-compensated digital compass
Example #3 – full position tracking from mobile phone data

## Slide 6: Mapping and navigation

## Slide 7: VR…

## Slide 8: AR…

## Slide 9: Motion capture…
Notes: https://www.xsens.com/products/xsens-mvn/

## Slide 10: Motion capture…

## Slide 11: Control and stabilisation…

## Slide 12: Automotive…

## Slide 13: “Quantified self”…

## Slide 14: Sports coaching…

## Slide 15: Sports coaching…
Notes: Snypr – Lacrosse training app …. Slip phone into holder on arm… Detect motion… Analyse….. Count reps….

## Slide 16: Sports coaching…
Notes: https://www.wareable.com/golf/zepp-2-offers-new-design-and-enhanced-coaching-2548

## Slide 17: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …

## Slide 18: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …
Ameasured = Asensor - R g
R is rotation matrix converting gravity vector g to sensor’s local (x,y,z) coordinates
Notes: See

## Slide 19: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …
Bmeasured = W (Rφ Rθ Rψ Bearth) + V
Rφ Rθ Rψ rotates the earth’s magnetic field by yaw (ψ), pitch (θ) and roll (ψ) angles to the sensor’s local (x,y,z) coordinates
W (3x3 matrix) and V (xyz-vector) are “soft iron” and “hard iron” distortions for ferromagnetic components that move with the sensor
Notes: Picture is from a blog post by Seb Madgwick, who wrote the seminal paper “An efficient orientation filter for inertial and intertial/magnetic sensor arrays” (30 Apr, 2010)
Blog post is: http://diydrones.com/forum/topics/magnetometer-soft-and-hard-iron-calibration

## Slide 20: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …

## Slide 21: Foucault’s gyroscope (1862)
Notes: In 1851, Leon Foucault famous pendulum rotated once per sidereal day – 23h56m at the poles.
But as you move down in latitude, the swing plane is at an angle to the rotation of the earth through the poles.
The rotation slowed down depending on the sine of the latitude.
In 1852, he build a gyroscope where the rotating mass maintained a fixed direction as the earth rotated.
It only ran for 10 minutes before slowing. This was enough to prove the principle.
Pictures are from http://tobin.pagesperso-orange.fr/PROBING_SPACE_Nelson.pdf

## Slide 22: ST124-M inertial platform for Saturn V (1965)
Notes: ST124-M inertial platform system

## Slide 24
Notes: IU-514 instrument unit
Silver sphere contains nitrogen for lubricating the gimbals.
Empty spot to the right is where the ST124-M gimbal unit would sit

## Slide 28: MEMS gyroscope (2016)
Notes: MEMS = Micromachined electromagnetic structure

## Slide 29: MEMS gyroscope (2016)
Notes: Image is from:
http://www.memsjournal.com/2011/01/motion-sensing-in-the-iphone-4-mems-gyroscope.html
http://memsjournal.typepad.com/.a/6a00d8345225f869e20148c7d54d63970c-pi

## Slide 30: Sensors in Metawear C PRO and BBC micro:bit
Accelerometer
Magnetometer
Gyroscope
Accelerometer Magnetometer
Notes: MetaWear Pro C from Mbient Labs (24 mm diameter). BBC MicroBit (43x52mm)

## Slide 31: Metaware C Pro – hardware
PCB: 24 mm diameter
sensors: 2 x 2 mm
[To be updated … These are Micro:Bit specs]
CPU
nRF51822 - Nordic Semiconductor
ARM Cortex-M0, 16k RAM, 256k flash
Interfaces
Bluetooth LE; radio; USB; push buttons
Sensors
Accelerometer MMA8652FC (NXP)
3 axis, 12-bit, up to 800Hz
6-180µA @ 2.4V
±2/4/8g (sens ±2.5%, offset ±33mg, noise 182µg/√Hz)
Magnetometer MAG3110 (NXP)
3 axis, 16-bit, up to 80 Hz
9-900µA @ 2.4V
±1000µT (sens 0.1µT, noise 0.25µT)

## Slide 32: BBC microbit – hardware
PCB: 43 x 52 mm
sensors: 2 x 2 mm
CPU
nRF51822 - Nordic Semiconductor
ARM Cortex-M0, 16k RAM, 256k flash
Interfaces
Bluetooth LE; radio; USB; push buttons
Sensors
Accelerometer MMA8652FC (NXP)
3 axis, 12-bit, up to 800Hz
6-180µA @ 2.4V
±2/4/8g (sens ±2.5%, offset ±33mg, noise 182µg/√Hz)
Magnetometer MAG3110 (NXP)
3 axis, 16-bit, up to 80 Hz
9-900µA @ 2.4V
±1000µT (sens 0.1µT, noise 0.25µT)

## Slide 33: Example #1 – Wireless motion logging

## Slide 34: Example #1 – BBC microbit code
# Transmit sensor data via radio
from microbit import *
import radio
header = "Time,AccX,AccY,AccZ,MagX,MagY,MagZ,Heading,Gesture\n“
def read_sensors():
"Sensor data as a comma-separated string with a newline"
t = running_time()
ax, ay, az = accelerometer.get_values()
g = accelerometer.current_gesture()
cx, cy, cz = compass.get_x(), compass.get_y(), compass.get_z()
h = compass.heading()
msg = '%d,%d,%d,%d,%d,%d,%d,%d,%s\n' % (t,ax,ay,az,cx,cy,cz,h,g)
return msg

## Slide 35: Example #1 – BBC microbit code
# Transmit sensor data via radio
from microbit import *
import radio
header = "Time,AccX,AccY,AccZ,MagX,MagY,MagZ,Heading,Gesture\n“
def read_sensors():
"Sensor data as a comma-separated string with a newline"
t = running_time()
ax, ay, az = accelerometer.get_values()
g = accelerometer.current_gesture()
cx, cy, cz = compass.get_x(), compass.get_y(), compass.get_z()
h = compass.heading()
msg = '%d,%d,%d,%d,%d,%d,%d,%d,%s\n' % (t,ax,ay,az,cx,cy,cz,h,g)
return msg
radio.config(length=100)
radio.on()
radio.send(header)
while True:
data = read_sensors()
radio.send(data)
sleep(25)

## Slide 36: Example #1 – BBC microbit code
# Transmit sensor data via radio
from microbit import *
import radio
header = "Time,AccX,AccY,AccZ,MagX,MagY,MagZ,Heading,Gesture\n“
def read_sensors():
"Sensor data as a comma-separated string with a newline"
t = running_time()
ax, ay, az = accelerometer.get_values()
g = accelerometer.current_gesture()
cx, cy, cz = compass.get_x(), compass.get_y(), compass.get_z()
h = compass.heading()
msg = '%d,%d,%d,%d,%d,%d,%d,%d,%s\n' % (t,ax,ay,az,cx,cy,cz,h,g)
return msg
radio.config(length=100)
radio.on()
radio.send(header)
while True:
data = read_sensors()
radio.send(data)
sleep(25)
# Relay radio data to host PC via USB
from microbit import *
import radio
radio.config(length=100)
radio.on()
uart.init(115000)
while True:
data = radio.receive()
if data:
uart.write(data)

## Slide 37: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
<class 'pandas.core.frame.DataFrame'>
Float64Index: 5860 entries, 12.9 to 246.1
Data columns (total 8 columns):
AccX 5860 non-null int64
AccY 5860 non-null int64
AccZ 5860 non-null int64
MagX 5860 non-null int64
MagY 5860 non-null int64
MagZ 5860 non-null int64
Heading 5860 non-null int64
Gesture 3760 non-null object
dtypes: int64(7), object(1)
memory usage: 412.0+ KB

## Slide 38: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
>>> accXYZ = df[['AccX','AccY','AccZ']]
>>> accXYZ.plot()
boiling
simmering
heating

## Slide 39: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
>>> accXYZ = df[['AccX','AccY','AccZ']]
>>> accXYZ.plot()
>>> g = accXYZ[50.0:200.0].mean()
>>> g
AccX 128.733753
AccY 802.477987
AccZ -636.926625
dtype: float64
>>> s = (accXYZ - g).pow(2).sum(axis=1)
>>> s.plot()
boiling
simmering
heating

## Slide 40: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
>>> accXYZ = df[['AccX','AccY','AccZ']]
>>> accXYZ.plot()
>>> g = accXYZ[50.0:200.0].mean()
>>> g
AccX 128.733753
AccY 802.477987
AccZ -636.926625
dtype: float64
>>> s = (accXYZ - g).pow(2).sum(axis=1)
>>> s.plot()
>>> import matplotlib.pyplot as plt
>>> plt.specgram(s, NFFT=512, Fs=100, noverlap=32)[3]
boiling
simmering
heating

## Slide 41: Data fusion
Combines data from multiple sensors
Reduces position errors when integrating accel/vel, correcting for sensor bias, drift, noise, nonlinearities
Deals with missing data points
Accelerometer
Magnetometer
Accelerometer
Gyroscope
Accelerometer
Magnetometer
Gyroscope
Electronic compass
(if acceleration = 0)
Inertial Measurement Unit (IMU)
(6 DoF – orientation, no absolute yaw)
Magnetic, Angular Rate, Gravity (MARG)
Attitude Heading Reference System (AHRS)
(9 DoF – orientation, absolute north)
Notes: Position errors proportional to t^3

## Slide 42: Example #2 – Tilt-compensating compass

## Slide 43: Example #3 – Kalman filter for 6-/9-DoF IMU

## Slide 44: Project ideas
1.

## Slide 45: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python
Motion sensors then and now – 1852, 1965, 2016
Example #1 – Wireless motion logging with BBC micro:bit
Data fusion – combining data from multiple sensors
Example #2 – micro:bit tilt-compensated digital compass
Example #3 – full position tracking from mobile phone data

## Slide 46: References
Github report accompanying this talk
http://github.com/stevesimmons/pyconuk-motion-sensor-data-fusion
BBC micro:bit (has accelerometer and magnetomer, no gyroscope)
MicroPython http://microbit-micropython.readthedocs.io
Mu editor / uFlash https://github.com/ntoll/mu http://uflash.readthedocs.org
MMA8652 accelerometer http://www.nxp.com/files/sensors/doc/data_sheet/MMA8652FC.pdf
MAG3110 magnetometer http://www.nxp.com/files/sensors/doc/data_sheet/MAG3110.pdf
http://www.nxp.com/files/sensors/doc/data_sheet/AN4083.pdf
Data fusion concepts
NXP sensor fusion toolbox (version 7.00, 18 August 2016)
http://www.nxp.com/products/sensors/nxp-sensor-fusion:XTRSICSNSTLBOX?tid=vansensorfusion
Datasheet http://cache.nxp.com/files/sensors/doc/data_sheet/XSFLK_DS.pdf
User guide http://cache.nxp.com/files/sensors/doc/user_guide/NSFK_Prod_UG.pdf
Electronic compass projects (accelerometer and magnetometer)
Circuit Cellar (2012) http://cache.nxp.com/files/sensors/doc/reports_presentations/ARTICLE_REPRINT.pdf
IMU/AHRS projects (accelerometer, gyroscope, magnetometer)
Madgwick’s algorithm (2010) https://www.samba.org/tridge/UAV/madgwick_internal_report.pdf
IMU Data Fusing http://www.olliw.eu/2013/imu-data-fusing/
9DoF Sensor Fusion https://github.com/kriswiner/MPU-6050/wiki/Affordable-9-DoF-Sensor-Fusion
Experimental Comparison of Sensor Fusion Algorithms for Attitude Estimation (A Cavallo et al IFAC 2014) http://www.nt.ntnu.no/users/skoge/prost/proceedings/ifac2014/media/files/1173.pdf
BerryIMU http://ozzmaker.com/berryimu-quick-start-guide https://github.com/mwilliams03/BerryIMU
MicroPython 6/9-DOF fusion (needs gyro -> not for BBC micro:bit) https://github.com/micropython-IMU/micropython-fusion

## Slide 47: They use comparable MEMS sensors
 | Phone OnePlus2 | Wearable MetaWear C PRO | Board BBC Micro:bit
Accelerometer | LIS3DSH (STM) | BMI160 IMU (Bosch) | MMA8652 (NXP Freescale)
Gyroscope | L3D20 (STM) |  | -
Magnetometer | MMC34160PJ (MEMSIC) |  | MAG3110 (NXP Freescale)
Source | My Sensors Android app |  | 
RF | Wifi, BT, BLE | BLE | BLE, radio
Memory |  |  | 16k RAM, 256k flash

## Slide 48: In technical terms, what do we want?
Real-time measurement of speed, orientation, position, …
Cheap, low-power sensors
Low-latency algorithms to clean up/pre-process raw data
Sensor-fusion – merge
High-level outputs – gestures, triggers

## Slide 49: Sensor degrees of freedom
6 DOF = 3-axis gyroscope and accelerometer = IMU
9 DOF = IMU + compass (magnetometer)
10 DOF = adds barometer (pressure)
11 DOF = add GPS receiver