## Slide 1: Python, Motion Sensors and Data Fusion PyCon UK, 15 September 2016
Stephen Simmons
mail@stevesimmons.com
https://github.com/stevesimmons/pyconuk-motion-sensor-data-fusion

## Slide 2: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap

## Slide 3: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python

## Slide 4: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python
Motion sensors then and now – 1852, 1965, 2016
Example #1 – Wireless motion logging with BBC micro:bit

## Slide 5: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python
Motion sensors then and now – 1852, 1965, 2016
Example #1 – Wireless motion logging with BBC micro:bit
Data fusion – combining data from multiple sensors
Example #2 – tilt-compensated digital compass
Example #3 – 9 DoF IMU from mobile phone data

## Slide 6: Mapping and navigation

## Slide 7: VR…

## Slide 8: AR…

## Slide 9: Motion capture…
Notes: https://www.xsens.com/products/xsens-mvn/

## Slide 10: Motion capture…

## Slide 11: Control and stabilisation…

## Slide 12: Automotive…

## Slide 13: “Quantified self”…

## Slide 14: Sports coaching…

## Slide 15: Sports coaching…
Notes: Snypr – Lacrosse training app …. Slip phone into holder on arm… Detect motion… Analyse….. Count reps….

## Slide 16: Sports coaching…
Notes: https://www.wareable.com/golf/zepp-2-offers-new-design-and-enhanced-coaching-2548

## Slide 17: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …

## Slide 18: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …
Axyz = Asensor - R g
R is rotation matrix converting gravity vector g to sensor’s local (x,y,z) coordinates
Notes: See

## Slide 19: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …
Bx,y,z = W Rφ Rθ Rψ Bearth + V
Rφ Rθ Rψ rotates the earth’s magnetic field by yaw (ψ), pitch (θ) and roll (φ) angles to the sensor’s local (x,y,z) coordinates
W (3x3 matrix) and V (xyz-vector) are “soft iron” and “hard iron” distortions for ferromagnetic components that move with the sensor
Notes: Picture is from a blog post by Seb Madgwick, who wrote the seminal paper “An efficient orientation filter for inertial and intertial/magnetic sensor arrays” (30 Apr, 2010)
Blog post is: http://diydrones.com/forum/topics/magnetometer-soft-and-hard-iron-calibration

## Slide 20: Types of sensors
Accelerometer
Linear acceleration plus gravity
Magnetometer
Local magnetic field
Gyroscope
Angular rotation rate
GPS
Absolute location (outdoor)
Pressure
Altitude (outdoor); relative height (indoor)
+ light, sound, touch, temperature, humidity, heart rate, …

## Slide 21: Foucault’s gyroscope (1862)
Notes: In 1851, Leon Foucault famous pendulum rotated once per sidereal day – 23h56m at the poles.
But as you move down in latitude, the swing plane is at an angle to the rotation of the earth through the poles.
The rotation slowed down depending on the sine of the latitude.
In 1852, he build a gyroscope where the rotating mass maintained a fixed direction as the earth rotated.
It only ran for 10 minutes before slowing. This was enough to prove the principle.
Pictures are from http://tobin.pagesperso-orange.fr/PROBING_SPACE_Nelson.pdf

## Slide 22: ST124-M inertial platform for Saturn V (1965)
Notes: ST124-M inertial platform system

## Slide 24
Notes: IU-514 instrument unit
Silver sphere contains nitrogen for lubricating the gimbals.
Empty spot to the right is where the ST124-M gimbal unit would sit

## Slide 28: MEMS gyroscope (2016)
Notes: MEMS = Micromachined electromagnetic structure

## Slide 29: MEMS gyroscope (2016)
Notes: Image is from:
http://www.memsjournal.com/2011/01/motion-sensing-in-the-iphone-4-mems-gyroscope.html
http://memsjournal.typepad.com/.a/6a00d8345225f869e20148c7d54d63970c-pi

## Slide 30: Sensors in Metawear CPRO and BBC micro:bit
Accelerometer
Gyroscope
Magnetometer
Accelerometer Magnetometer
Notes: MetaWear Pro C from Mbient Labs (24 mm diameter). BBC MicroBit (43x52mm)

## Slide 31: Metaware CPRO – hardware
PCB: 24 mm diameter
sensors: 2 x 2 mm
CPU
nRF51822 - Nordic Semiconductor
ARM Cortex-M0, 32k RAM, 256k flash
Interfaces
Bluetooth LE (stream up to 100 Hz)
Push button; 1 LED
Sensors
BMI160 (Bosch)
Accelerometer - 3 axis, 14-bit, up to 800Hz
Gyroscope – 3 axis, 16 bit
BMI155 Magnetometer (Bosch)
3 axis, 16-bit, up to 80 Hz
±1300µT (sens 0.3µT)
Pressure: 300-1100 hPa
Temperature: -40 to 85 °C
Light: 0.01 to 64k lux

## Slide 32: BBC microbit – hardware
PCB: 43 x 52 mm
sensors: 2 x 2 mm
CPU
nRF51822 - Nordic Semiconductor
ARM Cortex-M0, 16k RAM, 256k flash
Interfaces
Bluetooth LE; radio; USB Push buttons
Sensors
Accelerometer MMA8652FC (NXP)
3 axis, 12-bit, up to 800Hz
6-180µA @ 2.4V
±2/4/8g (sens ±2.5%, offset ±33mg, noise 182µg/√Hz)
Magnetometer MAG3110 (NXP)
3 axis, 16-bit, up to 80 Hz
9-900µA @ 2.4V
±1000µT (sens 0.1µT, noise 0.25µT)

## Slide 33: Example #1 – Wireless motion logging

## Slide 34: Example #1 – BBC microbit code
# Transmit sensor data via radio
from microbit import *
import radio
header = "Time,AccX,AccY,AccZ,MagX,MagY,MagZ,Heading,Gesture\n“
def read_sensors():
"Sensor data as a comma-separated string with a newline"
t = running_time()
ax, ay, az = accelerometer.get_values()
g = accelerometer.current_gesture()
cx, cy, cz = compass.get_x(), compass.get_y(), compass.get_z()
h = compass.heading()
msg = '%d,%d,%d,%d,%d,%d,%d,%d,%s\n' % (t,ax,ay,az,cx,cy,cz,h,g)
return msg

## Slide 35: Example #1 – BBC microbit code
# Transmit sensor data via radio
from microbit import *
import radio
header = "Time,AccX,AccY,AccZ,MagX,MagY,MagZ,Heading,Gesture\n“
def read_sensors():
"Sensor data as a comma-separated string with a newline"
t = running_time()
ax, ay, az = accelerometer.get_values()
g = accelerometer.current_gesture()
cx, cy, cz = compass.get_x(), compass.get_y(), compass.get_z()
h = compass.heading()
msg = '%d,%d,%d,%d,%d,%d,%d,%d,%s\n' % (t,ax,ay,az,cx,cy,cz,h,g)
return msg
radio.config(length=100)
radio.on()
radio.send(header)
while True:
data = read_sensors()
radio.send(data)
sleep(25)

## Slide 36: Example #1 – BBC microbit code
# Transmit sensor data via radio
from microbit import *
import radio
header = "Time,AccX,AccY,AccZ,MagX,MagY,MagZ,Heading,Gesture\n“
def read_sensors():
"Sensor data as a comma-separated string with a newline"
t = running_time()
ax, ay, az = accelerometer.get_values()
g = accelerometer.current_gesture()
cx, cy, cz = compass.get_x(), compass.get_y(), compass.get_z()
h = compass.heading()
msg = '%d,%d,%d,%d,%d,%d,%d,%d,%s\n' % (t,ax,ay,az,cx,cy,cz,h,g)
return msg
radio.config(length=100)
radio.on()
radio.send(header)
while True:
data = read_sensors()
radio.send(data)
sleep(25)
# Relay radio data to host PC via USB
from microbit import *
import radio
radio.config(length=100)
radio.on()
uart.init(115000)
while True:
data = radio.receive()
if data:
uart.write(data)

## Slide 37: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
<class 'pandas.core.frame.DataFrame'>
Float64Index: 5860 entries, 12.9 to 246.1
Data columns (total 8 columns):
AccX 5860 non-null int64
AccY 5860 non-null int64
AccZ 5860 non-null int64
MagX 5860 non-null int64
MagY 5860 non-null int64
MagZ 5860 non-null int64
Heading 5860 non-null int64
Gesture 3760 non-null object
dtypes: int64(7), object(1)
memory usage: 412.0+ KB

## Slide 38: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
>>> accXYZ = df[['AccX','AccY','AccZ']]
>>> accXYZ.plot()
boiling
simmering
heating

## Slide 39: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
>>> accXYZ = df[['AccX','AccY','AccZ']]
>>> accXYZ.plot()
>>> g = accXYZ[50.0:200.0].mean()
>>> g
AccX 128.733753
AccY 802.477987
AccZ -636.926625
dtype: float64
>>> s = (accXYZ - g).pow(2).sum(axis=1)
>>> s.plot()
boiling
simmering
heating

## Slide 40: Example #1 – Analyse data in IPython
# See Jupyter notebook analysis-kettle.ipynb
%matplotlib inline
import matplotlib
import pandas as pd
>>> df = pd.read_csv('data.csv')
>>> df['Time'] /= 1000.0 # ms to sec
>>> df.set_index('Time', inplace=True)
>>> df.info()
>>> accXYZ = df[['AccX','AccY','AccZ']]
>>> accXYZ.plot()
>>> g = accXYZ[50.0:200.0].mean()
>>> g
AccX 128.733753
AccY 802.477987
AccZ -636.926625
dtype: float64
>>> s = (accXYZ - g).pow(2).sum(axis=1)
>>> s.plot()
>>> import matplotlib.pyplot as plt
>>> plt.specgram(s, NFFT=512, Fs=100, noverlap=32)[3]
boiling
simmering
heating

## Slide 41: Project ideas
Orientation
Read accelerometer data
Figure out which simple gesture fits best (“falling”, “left”, “up”…)
Display first letter of the active gesture on the screen
Sports stats
Log accelerometer data while repeated a sport-related action (running, hitting tennis ball, …)
Plot the time series
Identify characteristic motion
Find decision rules to pinpoint time when motion occurred
Use decision rule to total sports stats (# actions, speed etc)

## Slide 42: Data fusion algorithms
Combine data from multiple sensors
Reduce position errors when integrating accel/vel
Correct for sensor bias, drift, noise, nonlinearities
Deal with missing data points
Accelerometer
Magnetometer
Accelerometer
Gyroscope
Accelerometer
Magnetometer
Gyroscope
Tilt-compensated electronic compass
(if acceleration = 0)
Inertial Measurement Unit (IMU)
(6 DoF – orientation, no absolute yaw)
Attitude Heading Reference System (AHRS)
Magnetic, Angular Rate, Gravity (MARG)
(9 DoF – orientation, absolute north)
Notes: Position errors proportional to t^3

## Slide 43: Example #2 – Tilt-compensating compass
Raw magnetometer data
# See analysis-tilt-compensation.ipynb
import numpy as np
import pandas as pd
import math
rad2deg = 180.0 / math.pi
# Data is collected via microbit data logger as the
# microbit is tilted up and down while pointed in
# approximately a constant heading.
df = pd.read_csv('data-compass-heading-with-tilt.csv')
df['Time'] /= 1000.0 # ms (int) to sec (float)
df.set_index('Time', inplace=True)
def magXYZ_plus_intensity(df):
'''Add column 'MagIntensity' to DataFrame df'''
m = df[['MagX','MagY','MagZ']].copy()
m['MagIntensity'] = m.pow(2).sum(axis=1).pow(0.5)
return m
magXYZ_plus_intensity(df).plot()

## Slide 44: Example #2 – Tilt-compensating compass
Calculated heading (degrees)
Raw magnetometer data
# See analysis-tilt-compensation.ipynb
import numpy as np
import pandas as pd
import math
rad2deg = 180.0 / math.pi
# Data is collected via microbit data logger as the
# microbit is tilted up and down while pointed in
# approximately a constant heading.
df = pd.read_csv('data-compass-heading-with-tilt.csv')
df['Time'] /= 1000.0 # ms (int) to sec (float)
df.set_index('Time', inplace=True)
def magXYZ_plus_intensity(df):
'''Add column 'MagIntensity' to DataFrame df'''
m = df[['MagX','MagY','MagZ']].copy()
m['MagIntensity'] = m.pow(2).sum(axis=1).pow(0.5)
return m
magXYZ_plus_intensity(df).plot()
# Simple compass heading (yaw angle = psi)
psi = rad2deg * np.arctan2(-df.MagY, df.MagX)
s = pd.Series(psi, index=df.index)
s.plot()

## Slide 45: Example #2 – Tilt-compensating compass
Calculated heading (degrees)
Raw magnetometer data
def compass_heading_tilt_comp(df):
"""Pandas Series with heading corrected for tilt.
This assumes the accelerometer is held still.
From the angle of gravity, infer the magnetometer's
tilt relative to the Earth's surface.
Undo the effects of tilt in the roll and pitch
directions, leaving a clean magnetic heading in
the yaw (Z) direction.
The input dataframe is assumed to have columns named
MagX, MagY, MagZ, AccX, AccY, AccZ.
"""
ax, ay, az = df.AccX, df.AccY, df.AccZ
mx, my, mz = df.MagX, df.MagY, df.MagZ
# Undo roll around X axis by angle phi
phi = np.arctan2(ay, az) # +/- 180 degrees
s, c = np.sin(phi), np.cos(phi)
az = ay*s + az*c
my, mz = (my*c - mz*s), (my*s + mz*c)
# Undo pitch around Y axis by angle theta
theta = np.arctan(-ax / az) # +/-90 degrees
s, c = np.sin(theta), np.cos(theta)
mx, mz = (mx*c + mz*s), (-mx*s + mz*c)
# Calculate yaw angle psi around Z axis
psi = np.arctan2(my, mx)
s = pd.Series(psi*rad2deg, index=df.index,
name='HeadingTiltCorrected')
return s

## Slide 46: Example #2 – Simple magnetometer calibration
Ideal readings lie on a perfect sphere
Pre- and post- calibration data
Bx,y,z = W Rφ Rθ Rψ Bearth + V where V = “hard iron”; W = “soft iron”
Proper calibration fits W to an ellipsoid.
To simplify the example today, don’t worry about rotation, just offset V and scale S:
V = (magXYZ.min() + magXYZ.max()) / 2
S = (magXYZ.max() - magXYZ.min()) / 2
magXYZ_cal = (magXYZ – V) / S

## Slide 47: Example #3 – Mobile phone sensor data
List sensors, manufacturers, specs, etc
My Sensors
Stream sensor data over wifi
IMU+GPS-Stream
Log sensor data to csv on phone
Physics Toolbox Suite
Or write your own app for processing sensor data locally

## Slide 48: Example #3 – Mobile phone sensor data
List sensors, manufacturers, etc
My Sensors
Stream sensor data over wifi
IMU+GPS-Stream
Log sensor data to csv on phone
Physics Toolbox Suite
Or write your own app for processing sensor data locally

## Slide 49: Example #3 – Mobile phone sensor data
List sensors, manufacturers, etc
My Sensors
Stream sensor data over wifi
IMU+GPS-Stream
Log sensor data to csv on phone
Physics Toolbox Suite
Or write your own app for processing sensor data locally

## Slide 50: Example #3 – Kalman filter for 9-DoF IMU
Diagram from NXP Sensor Fusion Library for Kinetis MCUs, release 7.00, August 2016

## Slide 51: Example #3 – Kalman filter for 9-DoF IMU
# Load 9-DoF sensor data as pandas DataFrame
df = pd.read_csv("data-IMU.csv")
names = 'Time,AccX,AccY,AccZ,GyroX,GyroY,GyroZ,MagX,MagY,MagZ'.split(',')
df.rename(columns=dict(zip(df.columns, new_names)), inplace=True)
df.set_index('Time', drop=False, inplace=True)
# Get data as numpy arrays that scikit-kinematics expects
aXYZ = df[['AccX','AccY','AccZ']].values
gXYZ = df[['GyroX','GyroY','GyroZ']].values
mXYZ = df[['MagX','MagY','MagZ']].values
# IMU using Kalman filter from scikit-kinematics
# http://work.thaslwanter.at/skinematics/html/index.html
rate = len(df) / (df.Time.max() - df.Time.min())
import skinematics as skin
quaternion_arr = skin.imus.kalman_quat(rate, aXYZ*9.81, gXYZ, mXYZ)
quaternion_obj = skin.imus.quat.Quaternion(quaternion_arr)
angles_arr = quaternion_obj.export('Fick') * 180/math.pi
angles_df = pd.DataFrame(angles_arr, columns=['phi', 'theta','psi'], index=df.index)
angles_df.plot()

## Slide 52: Project ideas
Orientation
Read accelerometer data
Figure out which simple gesture fits best (“falling”, “left”, “up”…)
Display first letter of the active gesture on the screen
Sports stats
Log accelerometer data while repeated a sport-related action (running, hitting tennis ball, …)
Plot the time series
Identify characteristic motion
Find decision rules to pinpoint time when motion occurred
Use decision rule to total sports stats (# actions, speed etc)
9 DoF IMU (Inertial Measurement Unit)
Find a Python IMU project on GitHub
Capture accel/mag/gyro data from mobile phone
Reformat the data and feed into the IMU
See how accurately this can track orientation/position using a Kalman filter

## Slide 53: Goals for today…
Why play with motion sensors?
tiny sensors + fun applications + cheap + smart algorithms in python
Motion sensors then and now – 1852, 1965, 2016
Example #1 – Wireless motion logging with BBC micro:bit
Data fusion – combining data from multiple sensors
Example #2 – tilt-compensated digital compass
Example #3 – 9 DoF IMU from mobile phone data

## Slide 54: References
Github report accompanying this talk
http://github.com/stevesimmons/pyconuk-motion-sensor-data-fusion
BBC micro:bit (has accelerometer and magnetomer, no gyroscope)
MicroPython http://microbit-micropython.readthedocs.io
Mu editor / uFlash https://github.com/ntoll/mu http://uflash.readthedocs.org
MMA8652 accelerometer http://www.nxp.com/files/sensors/doc/data_sheet/MMA8652FC.pdf
MAG3110 magnetometer http://www.nxp.com/files/sensors/doc/data_sheet/MAG3110.pdf
http://www.nxp.com/files/sensors/doc/data_sheet/AN4083.pdf
Data fusion concepts
NXP sensor fusion toolbox (version 7.00, 18 August 2016)
http://www.nxp.com/products/sensors/nxp-sensor-fusion:XTRSICSNSTLBOX?tid=vansensorfusion
Datasheet http://cache.nxp.com/files/sensors/doc/data_sheet/XSFLK_DS.pdf
User guide http://cache.nxp.com/files/sensors/doc/user_guide/NSFK_Prod_UG.pdf
Electronic compass projects (accelerometer and magnetometer)
Circuit Cellar (2012) http://cache.nxp.com/files/sensors/doc/reports_presentations/ARTICLE_REPRINT.pdf
IMU/AHRS projects (accelerometer, gyroscope, magnetometer)
scikit-kinematics http://work.thaslwanter.at/skinematics/html/index.html
Madgwick’s algorithm (2010) https://www.samba.org/tridge/UAV/madgwick_internal_report.pdf
IMU Data Fusing http://www.olliw.eu/2013/imu-data-fusing/
9DoF Sensor Fusion https://github.com/kriswiner/MPU-6050/wiki/Affordable-9-DoF-Sensor-Fusion
Experimental Comparison of Sensor Fusion Algorithms for Attitude Estimation (A Cavallo et al IFAC 2014) http://www.nt.ntnu.no/users/skoge/prost/proceedings/ifac2014/media/files/1173.pdf
BerryIMU http://ozzmaker.com/berryimu-quick-start-guide https://github.com/mwilliams03/BerryIMU
MicroPython 6/9-DOF fusion (needs gyro -> not for BBC micro:bit) https://github.com/micropython-IMU/micropython-fusion

## Slide 55: Python, Motion Sensors and Data Fusion PyCon UK, 15 September 2016
Stephen Simmons
mail@stevesimmons.com
https://github.com/stevesimmons/pyconuk-motion-sensor-data-fusion